## Slide 1: T Level In Digital Production, Design And Development
©TheComputingTutor

## Slide 2: Core Component – Content Area 7: Digital Environments
©TheComputingTutor

## Slide 3: Topic 7.1 – Physical Environments
©TheComputingTutor

## Slide 4: Specification Topics Covered
Section | Sub Section ID | Sub Section Content
7.1 Physical environments | 7.1.1 | Understand the features and characteristics of different types of physical computer system: ● personal computers ● mobile devices ● servers ● smart/internet-enabled devices.

## Slide 5: Topic 7.1.1 – Computer Systems
©TheComputingTutor

## Slide 6: Learning Objectives
To understand the features and characteristics of Personal computers ,servers and mobile devices.
To understand the features and characteristics of computer memory and storage.
To understand the features and characteristics of processors.
To understand the features and characteristics of network connectivity.
To understand the features and characteristics of smart devices.

## Slide 7: What is a Digital Environment?
A Digital Environment is where users can user and consume a range of digital services.
The Digital Environment is a mixture of hardware and software platforms.
Each of these platforms need to communicate with each other.
Digital Environments can be used at home or in business.
This unit will look at a range of hardware and software environments and how they interact.

## Slide 8: Features and Characteristics of Computer Systems
©TheComputingTutor

## Slide 9: Personal Computers
Personal computers are designed for home use.
They can be Desktop PC computers or laptops.
They all contain the same basic components:
A range of input and output devices.
One or more Hard Disk Drives (HDD).
Random Access Memory (RAM).
Cooling and a power supply.
A Motherboard that connects the internal components

## Slide 10: Laptop vs Desktop PC
Laptop Computer
Desktop computer

## Slide 11: Laptop vs Desktop Computers
Laptop
Powered from the Internal Battery or Mains power
Has built in keyboard, monitor and mouse
Desktop
Uses mains power only
Is in a fixed location
Can be carried around
Not easily upgradeable
Needs separate keyboard. monitor and mouse
Can add new components
Usually less powerful than desktops
Usually more powerful than laptops

## Slide 12: Features of Personal Computers - Size
PC cases come in a range of sizes.
This will determine the amount of space a PC will take on a desk.
This is usually called a Footprint.
Laptops usually take up smaller space on a desk.
A PC with a large case will take up more space than a PC with a smaller case.
If you have a large case size, you can fit more components inside it or add new components at a later data

## Slide 13: Case Size and Form Factor
The PC case sizes are referred to as the Form Factor.
This is directly linked to the size of the motherboard / mainboard.
A Small Form Factor PC can only fit a Small Form Factor motherboard.
This means it is restricted in the number of components that can be connected to it.

## Slide 14: Tower Case Sizes
Small Form Factor – Mini ITX case: Home use.
Mini Form Factor Tower – Mini ATX case: Home / Small business use.
Mid Form Factor Tower – ATX case: Small business / Enterprise use.
Full Form Factor Tower – E-ATX case: Enterprise / Developer / Server use.

## Slide 15: Different Tower Cases
Not very configurable
Relatively low power
Very configurable
Very high power

## Slide 16: Different Tower Case Specifications
 | Mini ITX | Micro ATX | ATX | e-ATX
Number of CPUs | 1 | 1 | 1 | 2
Number of Hard Drives | 1 | 1-2 | 1-3 | 1-6
Number of RAM slots | 1-2 | 1-3 | 4-8 | 6 - 8
Maximum RAM | 32GB | 64-128 GB | 512 GB | 2048GB
e-ATX cases are used for professional development machines or servers

## Slide 17: Full Tower vs Midi Tower Computers
Full Tower
Can have multiple processors
Will require a lot of power
Desktop
Usually only one processor
At most two hard drives
Can have multiple hard drives
Will need a lot of cooling
Will not use much power
Will need less cooling
Multiple slots for RAM chips
Usually has maximum 2 RAM chip slots

## Slide 18: Features of Personal Computers - Size
All PCs will require a separate monitor and keyboard.
This will increase the footprint of the PC.
If there are multiple monitors, this will also increase the footprint.
Multiple monitors mean that each screen can display a different application.
This will usually increase productivity, as there is no need to switch between applications.
Multiple monitor installations are more common in a business context than a home environment.

## Slide 19: Using Multiple Monitors
Word
Processor
Browser
Monitor 1
Monitor 2
User productivity is increased with two monitors
With two monitors you can have two applications open at the same time!

## Slide 20: Features of Personal Computers - Size
Some PCs contain all the core processing components within the monitor case.
This is usually called an All In One (AIO).
AIO PC’s have a very low footprint compared to desktop PC’s.
They are very good for home use / office use for basic programming tasks.
You cannot usually swap components within an AOI chassis.

## Slide 21: AIO vs Multiple Monitors
Still need separate keyboard and mouse
All system components behind monitor
Very large desktop footprint but each monitor can display a different application for increased productivity

## Slide 22: AIO vs Desktop PC
AIO
All components behind monitor
Can overheat due to lack of internal space
Desktop
Separate case for components
More powerful than AIO
Not very powerful
Not easy to upgrade
Can easily recirculate air for cooling
Very easy to upgrade
Small office footprint
Larger office footprint

## Slide 23: System Size Characteristics
Advantages
Bigger systems are more powerful
Bigger systems can be upgraded easily
Disadvantages
Bigger systems are more expensive
Bigger systems need more cooling
Smaller systems don’t take a lot of desk space
Smaller systems are usually cheaper
Bigger systems need a lot of desk space
Both will need separate keyboard and monitor

## Slide 24: Features and Characteristics of Computer Storage
©TheComputingTutor

## Slide 25: Features Of Personal Computers - Storage
All computers can store data persistently.
This means your data is preserved even if the power is turned off.
This type of storage is called NON-VOLATILE.
If you save your data to your hard drive and turn off your computer.
The next time you boot up your PC the data is still there.

## Slide 26: Internal Storage
Hard Drives usually come in one of two forms:
Magnetic Hard Drives.
Solid State Hard Drives.
Both have different principles of operation.

## Slide 27: Magnetic Hard Drives
These are a series of discs (platters) that contain an electromagnetic material.
The material is polarised to either NORTH or SOUTH.
This corresponds to 1 and 0.
The discs are split up into tracks.
Each track is split up into sectors.
The disc spins until the required sector is underneath the Read / Write head.

## Slide 28: Magnetic Hard Drive Components
platter
Sector cluster
Actuator arm
spindle
Read / write head
Direction of platter spin
Single sector
Direction of actuator arm movement
The different components of a Magnetic Hard Drive
Single Track

## Slide 29: How It Works
A magnetic hard disk contains multiple PLATTERS.
The data to be read is located in a SECTOR on a TRACK
The platters are constantly spinning, driven by a motor.
Typical spin speeds are 7200 Revolutions per minute (RPM).

## Slide 30: How It Works
The actuator arm moves side to side over each track.
The platter spins until the sector is underneath the Read / Write head of the actuator arm
The magnetic data is read as 1s and 0s into the computer.
Writing data to an HDD is the reverse of this process.

## Slide 31: HDD Issues
The platters are constantly spinning, so power is always needed.
The data cannot be read until the correct track and sector is located.
The actuator arm is driven by a mechanical motor.
HDD read write operations are slower than SSD operations.
Because HDDs are a stack of platters, they can be damaged easily if dropped or scratched.

## Slide 32: Solid State Hard Drives
In solid state hard drives, data is stored using NAND logic circuits.
These are printed onto a circuit board.
Each hard drive has a controller that arranges data into pages and blocks.
There are no moving parts, so SSDs are very fast, consume less power and are virtually silent.
They are currently more expensive than HDDs and have less data storage capacity.
SSD’s have a finite number of read / write operations, after which they stop working.
SSDs are more robust than HDDs and can survive being dropped or moved.

## Slide 33: SSD vs HDD Internal Storage
HDD
Cheaper than SSD
Slower to Read / Write
SSD
More expensive than HDD
Smaller storage capacity
Greater storage capacity
Consumes lots of power
Very fast Read / Write operations
Are robust and use very little power
Can be damaged
Will stop working after a certain number of R / W operations
Infinite number of R / W operations

## Slide 34: Research Task: Hard Drives
Try to find three examples of SSD and HDD drives from different manufacturers.
For each disk drive find out:
The size of the drive.
The cost of the drive.
Can you identify any patterns from your research?

## Slide 35: Worked Example: Hard Drives
Drive Manufacturer | Western Digital
Drive Name | WD Red Plus 8TB NAS Hard Drive
Drive Type | Magnetic Disk Drive
Drive Size | 8Tb
Drive Cost | £208.82 (correct in August 2024)
REFERENCE | https://www.ebuyer.com/2184020-wd-red-plus-8tb-nas-hard-drive-wd80efpx (correct in August 2024)

## Slide 36: Features and Characteristics of Computer Processors
©TheComputingTutor

## Slide 37: Features Of Personal Computers – Processor Speed
All programs consist of PROGRAM INSTRUCTIONS and PROGRAM DATA.
A Processor will load the instructions from main memory and will execute them.
The faster the processor speed, the more instructions can be executed every second.
This will increase the performance of the PC.

## Slide 38: The Processor
A motherboard with a single processor chip

## Slide 39: CPU Processor vs Core
A single CPU Processor chip can contain multiple Cores.
A Core can be thought of as a processor inside the CPU
The Core will decode and execute program instructions.
The CPU will contain small amounts of memory that can be shared between the cores. This is called Cache Memory.

## Slide 40: CPU Processor vs Core
SINGLE CORE CPU
MEMORY CONTROLLER
CACHE MEMORY
CORE
DUAL CORE CPU
MEMORY CONTROLLER
CACHE MEMORY
CORE 1
CORE 2
A Single versus a Dual Core CPU
Memory shared between cores

## Slide 41: Multiple Cores
Most CPUs today have four or six cores.
The more cores you have, the more programs can be run at the same time.
A single core CPU would only be able to effectively work on one program at once.
If the PC needed two or more programs running at the same time, the PC would struggle.
Remember – the Operating System Software is always running!

## Slide 42: Single Processor Single Core
SINGLE CORE
SINGLE PROCESSOR
PROCESS 1
SINGLE CORE
SINGLE PROCESSOR
PROCESS 1
PROCESS 2
This will work well
A single core CPU will struggle with
two or more programs

## Slide 43: Single Processor Multiple Core
CORE 1
SINGLE PROCESSOR
PROCESS 1
PROCESS 1
PROCESS 2
CORE 2
CORE 1
SINGLE PROCESSOR
CORE 2
Both cores can work on the one process – this is very fast
Both cores can work on each process – this is also very fast

## Slide 44: Processor Speed Characteristics
Advantages
More program instructions can be executed every second
The computer won’t slow down as more programs are opened
Disadvantages
Faster processors are expensive
Faster processors generate heat
Multiple cores mean a processor can work on two programs at once
Faster processors need a lot of cooling
Faster processors use more power

## Slide 45: Multiple Processors
Some computers can have more than one physical CPU chips.
Each processor will generate a lot of heat.
Multi CPU computers need a lot more cooling than single processor systems.
They also consume a lot more power.
They are very powerful and can run highly complex programs.
They are also very expensive.

## Slide 46: Multiple Processor Systems
The first processor chip
The second processor chip

## Slide 47: Multiple Processor Single Core
CORE 1
PROCESSOR 1
PROCESS 1
PROCESS 1
PROCESS 2
CORE 1
PROCESSOR 2
CORE 1
PROCESSOR 1
CORE 1
PROCESSOR 2
Both CPU’s can work on the one process – this is very fast
Both CPU’s can work on each process – this is also very fast

## Slide 48: Multiple Processor Multiple Core
CORE 1
PROCESSOR 1
PROCESS 1
PROCESS 1
PROCESS 2
PROCESSOR 2
CORE 2
CORE 1
CORE 2
CORE 1
PROCESSOR 1
PROCESSOR 2
CORE 2
CORE 1
CORE 2
All CPU’s and cores can work on the one process – this is the fastest
Both CPU’s and cores can work on both processes – this is very fast

## Slide 49: Research Task: Processors
Try to find three examples of CPU processors from different manufacturers.
For disk drive find out:
The number of CPU cores.
The clock speed of the CPU.
Can you identify any patterns from your research?
The cost of the CPU

## Slide 50: Worked Example: Processors
Processor Manufacturer | Intel
Processor | Intel Core i9 12900K Unlocked Processor
Number of Cores | 16
Clock Speed | 3.2 GHz
Processor Cost | £379.98 (correct in August 2024)
REFERENCE | https://www.ebuyer.com/1288877-intel-core-i9-12900k-unlocked-processor-bx8071512900k (correct in August 2024)

## Slide 51: Features and Characteristics of Computer Memory
©TheComputingTutor

## Slide 52: Features Of Personal Computers – Random Access Memory
Program instructions and data are loaded from the hard drive into a temporary storage area.
This is called Random Access Memory (or RAM).
It is also known as Main Memory.
We have looked at RAM in Content Area 2 when seeing how Lists and Arrays are stored.

## Slide 53: Features Of Personal Computers – Random Access Memory
RAM memory requires power to hold the transistor switches open or closed.
If the power is lost, all the switches will close and any data in RAM is lost.
RAM memory is VOLATILE.
If you lose power – any program or data in Main Memory will be lost.

## Slide 54: Loading Programs From The HDD
Empty
Main Memory
Empty
Empty
Empty
Instruction
Data
Instruction
program
DUAL CORE CPU
CACHE MEMORY
CORE 1
CORE 2
instruction
HDD
Programs are loaded from the HDD into RAM and then into the CPU Cache

## Slide 55: More RAM is Better
If you have a large amount of RAM, you can load the entire program into Main Memory.
Getting data out of the Hard Drive is the slowest part of the process.
Having program instructions and data in RAM means you can get these to the CPU faster.
The more RAM you have, the more programs you can have open at the same time.
If you run out of RAM, you will only be able to load fragments of a program from the Hard Drive.

## Slide 56: How Much RAM (2024)
In 2024, 8 – 16GB is good enough for most desktop PC’s running office applications.
For Gaming PCs, 16 - 32Gb is considered a reasonable amount of RAM.
Complex Graphics, Video Editing or processing of large datasets will need 256GB RAM.

## Slide 57: RAM Chips and Motherboard Slots
RAM is available as an integrated circuit chip.
RAM is available in multiples of 2GB.
RAM chips will need to plug into the Main Memory slots on a motherboard.
The more slots on the motherboard, the more RAM chips you can have.
If you have two slots you could potentially have 2 x 8GB, 2X 16GB, 1x 64GB.
The bigger the motherboard form factor, the more RAM chips you could install.

## Slide 58: RAM Chips and Motherboard Slots
Three individual RAM chips
Three Chips plugged into the motherboard

## Slide 59: RAM is READ / WRITE
Programs can be loaded from a HDD into Main Memory.
This process is called READING or LOADING.
Programs and data can also be saved from main memory to the HDD.
This process is called WRITING or SAVING.

## Slide 60: Writing Programs To The HDD
Empty
Main Memory
Empty
Empty
Empty
Instruction
Data
Instruction
program
DUAL CORE CPU
CACHE MEMORY
CORE 1
CORE 2
instruction
HDD
Programs are written from the CPU into RAM and then saved to the HDD

## Slide 61: Random Access Memory Characteristics
Advantages
More RAM means an entire program can be loaded from the hard drive
Disadvantages
RAM is VOLATILE
If the power is lost, any unsaved data will also be lost
Not enough RAM can dramatically slow down a PC
More RAM means multiple applications can run at the same time without slowing down
Supports READ WRITE operations

## Slide 62: Research Task: Main Memory
Try to find three examples of RAM memory from different manufacturers.
For memory chip find out:
The size of the memory.
The speed of the memory.
Can you identify any patterns from your research?
The cost of the memory

## Slide 63: Worked Example: Main Memory
Chip Manufacturer | Kingston
Chip Name | Kingston FURY Beast Desktop Memory for Gaming
RAM size | 64GB
RAM speed | DDR5 5600MHz
RAM cost | £149.99 (correct in August 2024)
REFERENCE | https://www.ebuyer.com/1419974-kingston-fury-beast-64gb-ddr5-5600mhz-ram-desktop-memory-for-gaming-kf556c40bbk2-64 (correct in August 2024)

## Slide 64: Features and Characteristics of Network Connectivity
©TheComputingTutor

## Slide 65: Features Of Personal Computers – Network Connectivity
All personal computers will now have the ability to connect to a local network.
This connection can either be wired (using Ethernet cables).
It could be wireless, using inbuilt wireless cards.
Most modern motherboards have wireless connectivity built.

## Slide 66: A PC With Wired and Wireless Connectivity
This PC is connected to the internet by an ethernet connection
There are two wireless networks available also

## Slide 67: Wired Connectivity Characteristics
Advantages
Substantially faster than wireless
More secure than wireless as the signal cannot be intercepted
Disadvantages
Limited by the length of the cable
Devices are in a fixed location
Cheaper than wireless – you just need the cables
If the cable breaks the network fails
As the cable gets longer the signal gets weaker
Can only have a finite number of devices on the network

## Slide 68: Wireless Connectivity Characteristics
Advantages
Less restriction on range
Can move devices around the network easily
Disadvantages
Security risk of eavesdropping
Slower than wired connection
Can have multiple devices on the network
Can get interference from walls
Hardware is more expensive

## Slide 69: Class Task 1 – Personal Computers
Work through all of the tasks on your worksheet.
Refer to your class notes or the lesson slides.
Compare your answer with the group.
TIME ALLOWED: 15 Minutes.

## Slide 70: Features and Characteristics of Mobile Devices
©TheComputingTutor

## Slide 71: Mobile Devices
Mobile devices are small, hand-held devices that contain computing capability.
These include most mobile phones, smartwatches and tablets.
These can either connect to a local or 4G / 5G network, or to other devices by Bluetooth.
Connectivity is mostly wireless.
All devices contain batteries that require charging.
Mobile devices are very good for consuming services, but not ideal for producing content.

## Slide 72: Mobile Device Issues
Sustainability is a great problem.
Consumers are required to update mobile devices regularly to get the latest security.
Recycling is an issue for old devices as thousands of tons of waste material is generated each year.
Obtaining materials is an issue for new devices – materials for the batteries, screen and circuit boards need to be extracted from the ground to meet the demand for new devices.
Security is another issue -mobile devices are now increasingly the target of hacking attempts.

## Slide 73: Mobile Device Characteristics
Advantages
Mobile devices are becoming increasingly powerful
Use RISC chips that generate little heat
Disadvantages
Battery life is a factor
Screen size not the biggest
Allow go-anywhere computing
Increasingly becoming targets for hackers
Almost impossible to upgrade components
Sustainability is a problem

## Slide 74: Features and Characteristics of Servers
©TheComputingTutor

## Slide 75: Servers
In the real world, a server is someone who provides a service.
Think for example of a waiter in a restaurant.
You can ask them to do something for you (this is a REQUEST).
They will go away and try to do it.
They will come back and give you an answer (this is a RESPONSE).

## Slide 76: Animation: A Waiter In A Restaurant
REQUEST
Can we have a drink?
RESPONSE
Sorry, we’re out of that!
SERVER
CLIENT
Can we have a drink?
Here you go!
Sorry, we’re out of that!
Possible
Responses
A REQUEST / RESPONSE model

## Slide 77: Servers
This is exactly how all servers work in the real world.
Each server will receive a REQUEST from a client.
The server will attempt to carry out that request.
If it can, the client will get the service asked for and may be notified with a RESPONSE.
If not, the client will be notified with a RESPONSE that the task HAS NOT been carried out.

## Slide 78: Servers and Queues
Again, like in the real world, there are usually more clients than servers.
A server will get multiple requests from one or more clients.
Each request will be put in a queue.
The server will deal with each request in order.

## Slide 79: Animation: Servers Will Queue Multiple Requests
REQUEST 1
SERVER
CLIENT 1
REQUEST QUEUE
CLIENT 2
CLIENT 3
REQUEST QUEUE
REQUEST 3
REQUEST 2
REQUEST 1
REQUEST 2
REQUEST 3

## Slide 80: Overloading A Server
If a server receives too many requests, it will appear as if it has stopped working.
In fact, it is still processing each request one at a time.
Your request is at the bottom of the queue.
The server will get to it eventually.
However, it looks like nothing is happening.
This is the basic principle of a DENIAL-OF-SERVICE attack.

## Slide 81: Server Characteristics
Advantages
Can deal with multiple requests from multiple clients
Operates across a network
Disadvantages
If the server fails, nothing works
Can provide a range of centralised services
Hardware and software can be expensive
Too many requests can overload the server

## Slide 82: Server Types
Servers can be both hardware and software.
You can install server software on server hardware.
Some server software can run on deskop PC’s.

## Slide 83: Server Types
You should be aware of the following server types and typical requests and responses:
File servers.
Database Servers.
Print Servers.
Mail Servers.
Web Servers.

## Slide 84: Class Task Worked Example – Web Server Requests and Responses
WEB SERVER | Server that accepts requests from a client for a web page or resource on a web page |  | 
REQUEST | Meaning | RESPONSE | Meaning
HTTP_GET | requests data from a specific resource | HTTP_RESPONSE | The web content that was asked for in the specific HTTP Request
HTTP_POST | sends client data to a server for processing |  | 
HTTP_PUT | sends client data to a server to replace a resource |  | 
HTTP_DELETE | deletes a requested resource |  | 

## Slide 85: Research Task: Servers
Try to find three examples of physical servers from different maufacturers.
For each server find out:
The number and speed of the CPU’s.
The amount of main memory and disk space.
Can you identify any patterns from your research?
The cost of the server.

## Slide 86: Worked Example: Servers
Server Manufacturer | Dell
Server Name | Smart Selection PowerEdge R7625 Rack Server
Number and size of CPU | 2 x AMD EPYC 2.70GHz 32 Core 128Mb Cache
RAM | 8 x 32Gb (256Gb total)
Disk Space | 2 x 1.6Tb SSD (3.2 Tb Total)
Cost | £17, 815.32 (correct in August 2024)
REFERENCE | https://www.dell.com/en-uk/shop/dell-servers-storage-networking/smart-selection-poweredge-r7625-rack-server-with-gpu-accelerators-for-ai-ml-hpc/spd/poweredge-r7625/per7625ai_ml_hpc (correct in August 2024)

## Slide 87: Class Task 2 – Servers
For each of the identified servers in your worksheet.
Try and identify as many REQUESTS and RESPONSES as you can.
Share your findings with the group.
TIME ALLOWED: 15 Minutes.

## Slide 88: Features and Characteristics of Smart Devices
©TheComputingTutor

## Slide 89: Smart Devices
A smart device is also called an Internet of Things (IoT) device.
This is where a device can communicate with a user or another device using a network.
The network can be a local network or the internet.
Communication usually takes place using either Wi-Fi or HTTP / HTTPS.

## Slide 90: Smart Devices
Smart Devices are so called because they have a range of remote-controlled functionality.
You can set an IoT home heating system to turn on from a networked device.
Smart devices can also notify a client should something happen.
A smart fridge can notify any connected devices that the door has been left open and the temperature has dropped.

## Slide 91: Smart Devices – Local Network
Local Network
IoT Device
Communication between client and IoT device over Wi-Fi Network

## Slide 92: Animation: Communicating With A Smart Device Over The Internet
Local
Network
IoT Device
Internet
HTTP Request
HTTP Request
HTTP Response
HTTP Response
Request sent over the internet
Request received by smart device
Response sent by smart device
Response received by client
Client sends a request to the IoT device, which then responds

## Slide 93: Animation: A Smart Device Notifying A Connected Device Over The Internet
Local
Network
IoT Device
Internet
HTTP Response
HTTP Response
HTTP Request
HTTP Request
Request sent over the internet
Request received by client
Response sent by client
Response received by smart device
IoT device sends a request to the Client, which then responds

## Slide 94: Request / Response Examples
Request Source | Request | Response
Client Device | Turn Camera On | OK
Client Device | Turn Camera Off | Operation Failed
Smart Device | Motion Sensor Activated | OK
Smart Device | Battery Low | OK
Smart Camera Request / Response Examples

## Slide 95: Smart Device Examples
Device | Examples | Client Operations | Device Notifications
Appliances | Fridges, washing machines | Turn On Turn Off | Task Complete Alarm error
Security | Camera, Doorbell | Turn On Record | Motion sensor activated Doorbell pressed
Wearables | Fitness monitors | Start recording | notify emergency services if blood pressure drops
 | health monitors | Set fitness goal | notify when goal reached
Inventory trackers | Stock Tracker Inventory Manager | check stock level check stock location record stock usage | notify when stock levels have dropped automatically reorder stock

## Slide 96: Class Discussion: Smart Devices
Do you have any smart devices in your home?
What do you use them for and how do you communicate with them?
TIME ALLOWED: 10 minutes.

## Slide 97: Class Discussion: Suggested Answers
Smart speakers like Amazon Alexa listen to voice commands.
Smart doorbells like ring notify you when someone presses the doorbell.
Smart home security cameras record things that move in the field of view.
Smart home heating systems can be turned on and set remotely.
Smart TV’s listen to voice commands and will suggest playback options.
Smart kitchen devices can be turned on and off remotely and can notify you if there are problems.

## Slide 98: IoT Security Risks
Most IoT devices come with a default username and password login details.
This is supplied by the manufacturer.
Most of these login details have now been obtained by hackers.
If these default login details are not changed by the user a hacker can gain access to this device.
It can the use the IoT device to send a request to other devices in the network.

## Slide 99: Animation: IoT Device Security Risks
Local
Network
IoT Device
Internet
HTTP Request
HTTP Request
Attacker
Attacker creates malicious HTTP request
malicious HTTP request received by Iot Device
IoT device attacks the real target on the network
IoT devices can be used to attack other devices on the network
IoT Device
Target

## Slide 100: Smart Device Characteristics
Advantages
Accessible anywhere
Can notify client when something happens
Disadvantages
Can be a security risk
Needs network or internet connection
Provides information in real time as it happens
Too many requests can overload the device

## Slide 101: Class Task 3 – Smart Devices
Work through all of the tasks on your worksheet.
Refer to your class notes or the lesson slides.
Compare your answer with the group.
TIME ALLOWED: 15 Minutes.

## Slide 102: Exam Style Questions
©TheComputingTutor

## Slide 103: Exam Questions
Each of your exam questions will start with a command word.
The type of command word will determine how you answer the question.
It will also determine how your marks will be awarded.
You need to be aware of the following command words.

## Slide 104: The ‘Name’ Command Word
This is the easisest command word to understand.
Here you simply list a number of different facts.
A two mark ‘Name’ question required two different facts.
Make sure the facts are different and not simply the opposite.
For example: “Switches are faster than hubs. Hubs are slower than switches”.
This is the same point just repeated from an opposite perspective.

## Slide 105: Name Question – How The Marks Are Awarded
A 2 Mark Name-Style Question
The first point
The second point
A 3 Mark Name-Style Question
The first point
The second point
The third point
3 marks
TOTAL
How to score marks in Name-Style questions
2 marks
TOTAL

## Slide 106: The ‘Explain’ Command Word
If you see a question with the command word ‘Explain’.
Each question will either be 2 marks or 4 marks.
You get ONE mark for identifying a point.
You get ONE mark expanding or explaining the point.

## Slide 107: Explain-Style Question – How The Marks Are Awarded
A 2 Mark Explain-Style Question
The point
The expansion
2 marks
A 4 Mark Explain-Style Question
First point
The expansion
2 marks
Second point
The expansion
2 marks
4 marks
TOTAL
How to score marks in Explain-Style questions
2 marks
TOTAL

## Slide 108: The ‘Describe’ Command Word
Here you need to have several points that are LINKED.
They need to be linked by joining words.
Joining words could be “and”, “because”, “therefore”, “either”, “allowing” etc.

## Slide 109: The ‘Describe’ Command Word
For example: Routers are good because they join networks together allowing larger networks to be built.
Routers are good (1 mark) .
Because they join networks (1 mark) .
Allowing larger networks to be built (1 mark) .
Each part is joined together .

## Slide 110: Describe-Style Question – How The Marks Are Awarded
A 2 Mark Describe-Style Question
The first point
The linked point
2 marks
A 3 Mark Describe-Style Question
The first point
The linked point
The linked point
3 marks
TOTAL
How to score marks in a Describe-Style questions
2 marks
TOTAL

## Slide 111: The ‘Discuss’ Command Word
This is getting more complicated.
You need to make a point that is relevant to the scenario.
If there are 4 marks you need to make 4 points that are relevant to the scenario.
This is reflected in the mark scheme.
‘Discuss’ style questions are all about the scenario.
‘Discuss’ style questions are usually 6 marks.

## Slide 112: The ‘Discuss’ Question Mark Scheme

## Slide 113: Get Maximum Marks – 6 Marks, 6 Facts!
Break the problem down into the right number of points
This is basically saying that if you have a 6 marks question you need to include 6 facts

## Slide 114: Get Maximum Marks – Always Refer To The Scenario
Always refer to the scenario and the business in your answer
This is basically saying that each of your facts must relate to the scenario and the business

## Slide 115: The Evaluate Command Word
This is an even more challenging question.
‘Evaluate’ Style questions are mini essays.
They are broken up into three parts.
Part 1 – list all the facts about each possible solution to problem scenario.
Part 2 – apply the solution facts to the problem scenario.
Part 3 – Come up with a conclusion saying which solution is best and why.
‘Evaluate’ style questions are either 9 or 12 marks.

## Slide 116: Evaluate-Style Question – How to organise your answer
A 9 or 12 Mark Evaluate-Style Question
List all the facts
Come up with a conclusion
Apply the facts to the scenario
How to score marks in an Evaluate-Style questions
9 marks
TOTAL

## Slide 117: The 9 Mark ‘Evaluate’ Question Mark Scheme

## Slide 118: Get Maximum Marks – List The Facts!
List as many facts as you can about the problem
List as many facts as you can

## Slide 119: Get Maximum Marks – Apply The Facts To The Scenario!
Apply the facts to the problem
Apply the facts to the problem

## Slide 120: Get Maximum Marks – Give A Conclusion Recommending A Solution!
Come up with a conclusion
Come up with a conclusion

## Slide 121: End of lesson: Exam Style Questions
At the end of your worksheet, there are some exam style questions.
You should be aiming for 1 mark in 1 minute.
Compare your answers with the answers provided.
TIME ALLOWED: 30 Minutes.

## Slide 122: Self-Check: Lesson Review
Can I explain the different types of computer hardware?
Can I explain the benefits and disadvantages of the different types of computer hardware?
Can I explain the different types of network connectivity?
Can I explain benefits and disadvantages of the different types of network connectivity?
Can I explain benefits and disadvantages smart devices?

## Slide 123: Further Reading
Websites
https://www.tutorialspoint.com/computer_fundamentals/computer_hardware.htm
https://www.tutorialspoint.com/computer_fundamentals/computer_components.htm
https://www.geeksforgeeks.org/random-access-memory-ram/
https://www.wired.com/story/how-to-set-up-smart-home/
https://www.javatpoint.com/server
https://www.theserverside.com/blog/Coffee-Talk-Java-News-Stories-and-Opinions/HTTP-methods
Videos
https://www.youtube.com/watch?v=HB4I2CgkcCo
https://www.youtube.com/watch?v=d86ws7mQYIg
https://www.youtube.com/watch?v=UjCDWCeHCzY
Textbook: pp165 - 166

## Slide 124
No part of this publication may be reproduced, distributed, or transmitted in any form or by any means, including photocopying, recording, or other electronic or mechanical methods, without the prior written permission of the TheComputingTutor Ltd.